## Slide 1: Low-Power Analog Bayesian Classifier for Diabetes Detection
Charalampos Papadopoulos, ECE, NTUA

## Slide 2: Table of contents 01 04 02 05 03 06
Introduction
Initial Bump Design
Updated Bump Design
Classifier Analysis
Inference
Conclusions

## Slide 3: Introduction
Analog Classifiers
Hardware equivalent of software-based ML classifiers
Built using Bump Circuits + Bayesian/Gaussian models
Can directly classify analog input signals
Why Analog?
Ultra-low power – ideal for edge/wearable devices
Real time processing of sensor outputs
Application: Diabetes Detection
Diabetes = major global healthcare challenge
Goal: enable smart, low-power medical wearables.
Stepping stone for advanced health monitoring.

## Slide 4: 2. Initial Bump Design

## Slide 5: 2.1 – Delbruck’s Design
Proposed by T. Delbruck in 1991
Two main blocks: Differential Input and Assymetric Current Correlator
Sub-threshold operation
Generates Gaussian-like current output
and control the height and the mean value, respectively.
Quantity S is given as such:
is the slope factor and is the input voltage
Theoretical tunability

## Slide 6: 2.2 – Tunability of original bump
sweep
sweep
sweep

## Slide 7: 3. Updated Gaussian Bump Design

## Slide 8: 3.1 Current Mirror
Cascoded Current Mirror
Opamp Feedback Current Mirror
Biases the differential input
Finite output resistance source fluctuations leading to bad performance when shifting to lower values
Mitigations
  Increase channel length (L);
  Change configuration

## Slide 9: 3.2 – Updated Design
Differential Difference Pair (DDP):
Used as high-linearity voltage-to-current converter
Provides tunability and better common-mode rejection than a simple differential pair
and are bulk controlled
Sizing Considerations:
  W/L 1 with larger devices
  in order to eliminate offset
Symmetric Current Correlator (SCC):
Eliminate asymmetries caused by original design
Sizing considerations:
  Keep all transistors in the subthreshold region
  Larger W offers more voltage headroom

## Slide 10: 3.3 – Fingers and Multipliers for the SCC
F = 1, m = 1, 2, 4, 6
F = 2, m = 1, 2, 4, 6
F = 8, m = 10

## Slide 11: 3.4 – Tunability of our design
sweep
sweep
sweep

## Slide 12: 4. Classifier Architecture

## Slide 13: 4.1 – Theoretical Models
Gaussian Mixture Model (GMM):
Each class represented as a mixture of Gaussian functions
Probability density for input x:
Bayesian Classification:
Posterior probability
Decision rule: assign x to class with highest posterior probability

## Slide 14: 4.2 – Hardware Implementation
Implements Bayesian model: maps input features to class probabilities
Each class: n cascaded Bump circuits (n = number of input features; 11 for diabetes dataset)
  Cascaded: output of one bump serves as input to the next, multiplying the feature likelihoods to compute the joint probability.
  Each feature is converted into and values based on the dataset and code preprocessing
Each class outputs , with peak magnitude indicating the likelihood of belonging to that class
Winner-Take-All (WTA) circuit performs the argmax operator
Digital output suitable for further processing

## Slide 15: 5. Inference

## Slide 16: 5.1 – The Diabetes Dataset
Samples: Real-world patient data with multiple risk factors
Features (11 total):
  Demographics: Gender, Age, BMI
  Kidney function: Urea, Creatinine
  Glucose control: HbA1c
  Lipid profile: Chol, TG, HDL, LDL, VLDL
Target Classes (multi-class):
  0 = Non-Diabetic
  1 = Diabetic
  2 = Predict-Diabetic (at risk)
Features vary in scale and range → require normalization & mapping to circuit parameters ( and
Chosen for relevance: Diabetes = a critical health issue with global prevalence

## Slide 17: 5.2 – Performance Summary
Performance Summary
Software vs Hardware
Method | Best | Worst | Mean | Std.
Software | 0.99 | 0.87 | 0.93 | 0.03
Hardware | 0.89 | 0.75 | 0.79 | 0.03
Technology | Power Supply | Power Consumption | Classification Speed
130nm | 0.6V | 114nW | 20K

## Slide 18: 6. Overview & Conclusions
Results
Tested on a real diabetes dataset
Achieved 80% accuracy (vs. 93% in software)
Ultra-low power: 114 at 0.6 V supply
Key Takeaway
Proof-of-concept for low-power, real-time medical classifiers
Potential path toward smart wearable devices for health monitoring
Future work
Improve accuracy with extended feature handling
Integration with on-chip sensors & larger datasets

## Slide 19: Thank you!
Do you have any questions?
harrispap10@gmail.com